## Slide 1
DIPARTIMENTO DI INGEGNERIA ELETTRICA E TECNOLOGIE DELL’INFORMAZIONE
SCUOLA POLITECNICA E DELLE SCIENZE DI BASE
PLANNING AND CONTROL FOR A FULLY ACTUATED HEXACOPTER
Federico Esposito Prof. P38000142 Fabio Ruggiero
Riccardo Aliotta Academic Year: P38000143 2022/2023
FINAL PROJECT FIELD AND SERVICE ROBOTICS

## Slide 2
2/33
SUMMARY
Description of the Tilted Hexacopter
Allocation matrix
Environment design
Path planning
Trajectory planning
Control problem
  RPY and Coordinate-free Estimators
  Geometric Control
  Hierarchical Control
  Passivity-based Control
  Feedback Linearization Control
Conclusion

## Slide 3
3/33
DESCRIPTION OF THE TILTED HEXACOPTER
The robot we have considered is a hexacopter with non coplanar propellers with a cant angle of ±20°.
Thanks to the configuration of its 6 propellers, it is fully actuated.
Coordinate-free model:
RPY model:
The 0-th propeller is the red one on the right in the picture; it spins counterclockwise and its cant angle is 20°.
Adjacent propellers have opposite rotation directions and opposite cant angles.

## Slide 4
4/33
ALLOCATION MATRIX (1)
We have found the relationship between the propellers’ thrusts and the wrench applied on the robot.
Assuming that the thrust of a propeller is proportional to the square of its rotation speed, we then found the mapping between the rotor speeds and the wrench.
The matrix found is and full rank, proving the full actuation.
We’ve chosen a NED body frame and have put a reference frame in the center of each propeller, at a position and at an orientation in the body frame.
Useful robot parameters:
Expression of the i-th column of the matrix:

## Slide 5
5/33
ALLOCATION MATRIX (2)
Numerical value of the matrix after swapping the rows to have a wrench that starts with forces and ends with torques:
Multiplying the inverse of the matrix for the control wrench we get the propellers’ thrusts; then dividing by and extracting the root square we get the rotor speeds.
Due to the sign of in the UAV model, when converting the control forces into rotor speeds we first need to invert their sign.
In case a propeller needs to generate a negative thrust we must apply the absolute value before extracting the root square, and then we invert the rotation direction adding a minus sign to the rotor speed.

## Slide 6
6/33
The environment has been designed with an industrial inspection scenario in mind, yet simplified.
The task imagined is that of inspecting a piece of machinery (the starting point) and navigating the environment to get back to the ground station (the goal).
Custom meshes have been used to describe the obstacles, and then these have been placed in the environment through the use of an OccupationMap.
To obtain the collision-free space, the map has been inflated to account for the radius of the drone, then discretized with the use of a simple 3-dimensional matrix, where each cell represented a section of space measuring .
Environment designed for the simulation.
ENVIRONMENT DESIGN

## Slide 7
7/33
The path planning algorithm is an extension on three dimensions of the already seen Bilateral RRT algorithm with some minor variations, as both the starting and ending point are considered in the same roadmap for the sake of q_near.
If after a set amount of attempts the two trees can’t be connected, some retries are issued until a connection is found or the maximum total tries are exceeded.
The path is then stored as a matrix made of three columns and as many rows as there are points, and it is passed on to the trajectory planner.
Environment representation with the planned path.
PATH PLANNING

## Slide 8
8/33
The planner is very simple, as it assumes to move the drone in a segment from point to point and stopping at every point, while for the orientation the angles we’re able to control (all three RPY angles for the Feedback Linearization Control, only the Yaw for the others) are increased by a fixed amount for every segment crossed (the simulations were conducted with a 5° increase).
TRAJECTORY PLANNING
The time law is then obtained by using 5-th order polynomials, in order to have both null velocity and null acceleration in the starting and goal point for every segment of the trajectory.
On the side are the resulting time laws, where the angular variables appear as one as they are equal.

## Slide 9
9/33
After defining the trajectory and the time laws, they must be passed as reference to the drone controller. We have designed and tested four different controllers, three of which we’ve seen during the course (Hierarchical, Geometric and Passivity-based) and one designed by us that exploits the tilted drone’s full actuation through a feedback linearization approach.
In order to use the controllers made for the planar multicopter on the tilted we adopted, which takes as input forces on all the three axes, we need to pass the computed desired thrust as z-force component, while setting as null the x and y force components.
Where deemed necessary, additional integral actions have been added to the scheme for robustness and for error convergence, while the output wrench has been saturated. Moreover, for every controller an estimator has been designed, implemented and integrated in the control loop. Different controls, however, could be based on different model descriptions, and so also the estimator needs to vary accordingly.
CONTROL PROBLEM

## Slide 10
10/33
The estimators were implemented in the form seen during the course and of the third order, while the transfer function that describes their working was designed based on the controller, changing the position of the triple pole .
For the controllers based on the RPY drone model, the momentum is computed from the mass of the drone , the matrix , the drone velocity and the derivative of the Euler angles . The value of was chosen as 100.
RPY AND COORDINATE-FREE ESTIMATORS
For the controllers based on the coordinate-free drone model, instead, the momentum is computed from the mass of the drone , the drone velocity , the inertia matrix and the angular velocity . The value of was chosen as 50.

## Slide 11
11/33
The goal of the Geometric Control is to control the thrust and the reduced orientation to stabilize the tracking of the linear part, while using the rest of the rotation matrix to get the desired heading direction This is achieved by applying a feedback linearization on the angular part in an inner-loop, and computing thrust and desired reduced orientation in an outer-loop.
The use of the estimator and the integral actions on both the loops guarantees robustness and no position error at steady state.
Control gains:
= ,
= ,
GEOMETRIC CONTROL

## Slide 12
12/33
GEOMETRIC CONTROL (CONTROL ERRORS)

## Slide 13
13/33
GEOMETRIC CONTROL (CONTROL INPUTS)

## Slide 14
14/33
GEOMETRIC CONTROL (REFERENCE ANGLES)

## Slide 15
15/33
GEOMETRIC CONTROL (ESTIMATES)

## Slide 16
16/33
HIERARCHICAL CONTROL
The goal of the Hierarchical Control is to reach two linear subsystems coupled with a nonlinear interconnection term: to achieve that we apply a feedback linearization on the angular part in the inner-loop, while in the outer-loop we compute a desired acceleration vector and then from it obtain the force and the angular references and which aren’t provided from the planner.
The use of the estimator and the integral actions on both the loops guarantees robustness and no error at steady state.
Control gains:
obtained with place, pole in -2
obtained with place, pole in -20

## Slide 17
17/33
HIERARCHICAL CONTROL (CONTROL ERRORS)

## Slide 18
18/33
HIERARCHICAL CONTROL (CONTROL INPUTS 1)

## Slide 19
19/33
HIERARCHICAL CONTROL (CONTROL INPUTS 2)

## Slide 20
20/33
HIERARCHICAL CONTROL (REFERENCE ANGLES)

## Slide 21
21/33
HIERARCHICAL CONTROL (ESTIMATE)

## Slide 22
22/33
PASSIVITY-BASED CONTROL
The goal of the Passivity-based Control is to avoid the feedback linearization in the angular part: instead we build an inner-loop that establishes a passive relationship between the estimation error on the torque and the coupled error variable .
The outer loop is the same as the one seen in the Hierarchical Control.
Other than the estimator, this controller only needs an integral action on the linear part to have null errors at steady state.
Control gains:

## Slide 23
23/33
PASSIVITY-BASED CONTROL (CONTROL ERRORS)

## Slide 24
24/33
PASSIVITY-BASED CONTROL (CONTROL INPUTS 1)

## Slide 25
25/33
PASSIVITY-BASED CONTROL (CONTROL INPUTS 2)

## Slide 26
26/33
PASSIVITY-BASED CONTROL (REFERENCE ANGLES)

## Slide 27
27/33
PASSIVITY-BASED CONTROL (ESTIMATE)

## Slide 28
28/33
FEEDBACK LINEARIZATION CONTROL
With the Feedback Linearization Control we can finally exploit the tilted drone’s full actuation and thus use the full wrench as a control input.
The inner-loop is the same as the Hierarchical Control, while for the outer loop we simply cancel the system’s dynamics and then apply a virtual control input.
This time the integral action has been applied only to the angular part; both loops make use of the estimator.
All control gains are taken from the Hierarchical Control, with the exception of

## Slide 29
29/33
FEEDBACK LINEARIZATION CONTROL (CONTROL ERRORS)

## Slide 30
30/33
FEEDBACK LINEARIZATION CONTROL (CONTROL INPUTS)

## Slide 31
31/33
FEEDBACK LINEARIZATION CONTROL (ESTIMATE)

## Slide 32
32/33
CONCLUSIONS
We can conclude that all controllers performed in a more than satisfactory way, but the Geometric Control has many robustness issues. Moreover, for the intended scope of the drone’s tasks, there is no need for acrobatic flight, and for these reasons the use of this controller is not preferrable.
Among the RPY controllers, while the performances are all more than acceptable, the Feedback Linearization Controller has the best overall performances, with similar errors to the other controllers and with estimates and control inputs free of overshoot. Moreover, the full actuation of the drone itself and the exploitation of this by the controller makes it much more dexterous if compared to the other ones. For these reasons, the preferrable choice for a physical implementation of this kind of drone (among the analyzed controllers) should be the FBL.
Through the already computed rotor velocities we could also directly command a simulated (or real, for this matter) drone without too much code conversion effort thanks to MATLAB’s integrated code generation.

## Slide 33
33/33
THANKS FOR THE ATTENTION